## Slide 1
DIGITAL LOGIC PROJECT
Digital Door
Access System
Using Combination Logic
Presented by Team - 07
Manideep – 2620030560 · Aarush – 2620030563
Neelagreeva – 2620030564 · Swarajith – 2620030583
Hansika – 2620030551 · Section: 11
01 / 08

## Slide 2
DIGITAL LOGIC PROJECT
Team - 07
INTRODUCTION
Access control
Introduction and objective
The problem
Conventional keys can be lost, copied, or shared without visibility.
The idea
A digital door access system takes an entered code and decides, using logic gates, whether to unlock.
The approach
Build the decision circuit from basic gates, simulate it in Logisim and verify it with a truth table.
Objective: design and simulate a combinational logic circuit that unlocks the door only for the valid input code (A = 1, B = 0, C = 1) and rejects every other combination.
02 / 08

## Slide 3
THEORY
Team - 07
LOGIC GATES
Gates & Boolean logic
Theory and logic circuit
1
AND gate: the output is 1 only when all of its inputs are 1.
2
NOT gate: inverts its input, so 0 becomes 1 and 1 becomes 0.
3
B goes through a NOT gate, then A, NOT B and C enter a 3-input AND gate.
4
Y = A · B′ · C, so the door unlocks only for A = 1, B = 0, C = 1.
Combinational logic: the output depends only on the present inputs, with no memory.
03 / 08

## Slide 4
OPERATION
Team - 07
SYSTEM FLOW
Input to output
How the access system works
Valid code entered
A = 1, B = 0, C = 1: the NOT gate makes B′ = 1, so all three AND inputs are 1.
Y = 1 and the door unlocks.
Any other code
At least one AND input is 0, so Y = 0 and the door stays locked.
The A = B = C = 0 test in Logisim is one such case.
Combinational design: the decision follows the inputs instantly and stores no state.
04 / 08

## Slide 5
LOGISIM
Team - 07
CIRCUIT DESIGN
Built in Logisim
Circuit design in Logisim
Components used
Three input pins (A, B, C), a NOT gate on B, a 3-input AND gate and one output pin Y.
Bright green wires carry logic 1; dark green wires carry logic 0.
Working of the circuit
B is inverted, so the AND gate receives A, B′ and C.
Y = 1 only when A = 1, B = 0 and C = 1; that output unlocks the door.
Logisim shows every wire’s logic level live, so the design can be tested one input pattern at a time.
05 / 08

## Slide 6
SIMULATION
Team - 07
RESULTS
Truth table
Simulation results
What the simulation shows
With A = B = C = 0, the NOT gate makes B′ = 1, but A and C are 0, so Y = 0.
Of the 8 input combinations, only A = 1, B = 0, C = 1 gives Y = 1.
Result: the simulation matches the truth table; only code 101 unlocks the door.
A | B | C | B′ | Y
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0
Case shown in the Logisim screenshot
The only valid code (Y = 1)
Logisim run: A = B = C = 0 gives Y = 0 (access denied).
06 / 08

## Slide 7
DIGITAL LOGIC PROJECT
Team - 07
CONCLUSION
Outcome and scope
Conclusion and applications
01
Outcome
A 3-input access circuit was designed and simulated in Logisim.
Output Y = 1 only for A = 1, B = 0, C = 1.
The other seven input combinations are denied.
02
Applications
Home and office door locks
Keypad and digital-code entry panels
Lockers, safes and restricted rooms
03
Improvements
Extend to a longer 4-bit or 8-bit access code.
Add flip-flops to count wrong attempts and raise an alarm.
Drive a real lock through a microcontroller or FPGA.
Result: a simple, testable combinational design that shows how basic gates make a door-access decision.
07 / 08

## Slide 8
DIGITAL LOGIC PROJECT
Thank You
Presented by Team - 07
Manideep · Aarush · Neelagreeva · Swarajith · Hansika
GitHub link - https://github.com/Neelagreeva/DDCA-Digital-Door-Access-System-by-Team---07
08 / 08